## Slide 1
Reservoir modeling using Gaussian mixture models

## Slide 2: Introduction
Many linear inverse problems are solved using a Bayesian approach assuming Gaussian distribution of the model.
We show the analytical solution of the Bayesian linear inverse problem in the Gaussian mixture case.
Some applications to reservoir modeling are presented (reservoir properties estimation and simulation)

## Slide 3
Introduction
In reservoir modeling we aim to model rock properties: porosity, sand/clay content, saturations.
Rock properties cannot be directly measured away from the wells. The main source of information are seismic data.
Inverse problem
Seismic data
Porosity
Notes: Seismic dataset records information about the elastic contrasts in the subsurface. Seismic attributes depend on rock properties.

## Slide 4
Introduction
The seismic forward model can be linearized and the model linking velocities and rock properties is almost linear.
Rock properties can be described by a Gaussian Mixture (GM) model.

## Slide 5: Introduction
– 4
Well data
In traditional methods, when we observe a significant overlap in the prior distribution it is difficult to make a choice on the cut-off
P-wave velocity (m/s)
Porosity (v/v)
Sand content
P-wave velocity (m/s)
Porosity (v/v)

## Slide 6
– 4
Introduction
The seismic forward model can be linearized and the model linking velocities and rock properties is almost linear.
Rock properties can be described by a Gaussian Mixture (GM) model.
The goal is to estimate reservoir properties as a solution of a Bayesian GM inverse problem.

## Slide 7: Gaussian mixture models
A random vector m is distributed according to a Gaussian Mixture Model (GMM) with L components when the probability density is given by:
where each single component is Gaussian:
and the additional conditions
Example of 1D mixture with L=2 components (PDF and histogram of N random samples)

## Slide 8: Gaussian mixture models
Gaussian Mixture distribution
Weights, means and covariance matrices estimated by EM method (Hastie, Tibshirani, Friedman, The Elements of Statistical Learning, 2009)

## Slide 9: Linear inverse problems (Gaussian)
– 7
Linear inverse problem

## Slide 10: Linear inverse problems (Gaussian)
– 7
Linear inverse problem
If
then