## Slide 1
LAWS OF THERMODYNAMICS

## Slide 2
 In physics, thermodynamics is the study of energy conversion between heat and mechanical work, and subsequently the macroscopic variables such as temperature, volume and pressure. The starting point for most thermodynamic considerations are the laws of thermodynamics, which postulate that energy can be exchanged between physical systems as heat or work. They also postulate the existence of a quantity named entropy, which can be defined for any isolated system that is in thermodynamic equilibrium. In thermodynamics, interactions between large ensembles of objects are studied and categorized. Central to this are the concepts of system and surroundings. A system is composed of particles, whose average motions define its properties, which in turn are related to one another through equations of state. Properties can be combined to express internal energy and thermodynamic potentials, which are useful for determining conditions for equilibrium and spontaneous processes.

## Slide 3
showing input from a heat source (boiler) on the left and output to a heat sink (condenser) on the right. Work is extracted, in this case by a series of
pistons
TYPICAL THERMODYNAMICS ENGINE

## Slide 4: LAWS OF THERMODYNAMICS
The field of thermodynamics studies the behavior of energy flow in natural systems. From this study, a number of physical laws have been established. The laws of thermodynamics describe some of the fundamental truths of thermodynamics observed in our Universe. Understanding these laws is important to students of Physical Geography because many of the processes studied involve the flow of energy.

## Slide 5: ZEROTH LAW
If two thermodynamic systems are each in thermal equilibrium with a third, then they are in thermal equilibrium with each other.
When two systems are put in contact with each other, there will be a net exchange of energy between them unless or until they are in thermal equilibrium. That is the state of having equal temperature. Although this concept of thermodynamics is fundamental, the need to state it explicitly was not widely perceived until the first third of the 20th century, long after the first three principles were already widely in use. Hence it was numbered zero -- before the

## Slide 6
The Zeroth Law asserts that thermal equilibrium, viewed as a binary relation, is a
transitive relation (and since any system is always in equilibrium with itself and if a system is in equilibrium with another, the latter is in equilibrium with the former, it is furthermore an equivalence relation).

## Slide 8
Energy can neither be created nor destroyed.
It can only change forms.
In any process in an isolated system, the total energy remains the same.
For a thermodynamic cycle the net
heat supplied to the system equals the net work done by the system.

## Slide 9
 The First Law states that energy cannot be created or destroyed; rather, the amount of energy lost in a steady state process cannot be greater than the amount of energy gained. This is the statement of conservation of energy for a thermodynamic system. It refers to the two ways that a closed system transfers energy to and from its surroundings – by the process of heating (or cooling) and the process of mechanical work. The rate of gain or loss in the stored energy of a system is determined by the rates of these two processes. In open systems, the flow of matter is another energy transfer mechanism, and extra terms must be included in the expression of the first law.

## Slide 10: FUNDAMENTAL THERMODYNAMIC
plied to the syst
RELATION
The first law can be expressed as the fundamental thermodynamic relation:
Heat supplied to a system = increase in internal energy of the system + work done by the system
Increase in internal energy of a system = heat sup em - work done by the system
Here, E is internal energy, T is temperature, S is entropy, p is pressure, and V is volume. This is a statement of conservation of energy: The net change in internal energy (dE) equals the heat energy that flows in (TdS),

## Slide 12: SECOND LAW
The entropy of an isolated system consisting of two regions of space, isolated from one another, each in thermodynamic equilibrium in itself, but not in equilibrium with each other, will, when the isolation that separates the two regions is broken, so that the two regions become able to exchange matter or energy, tend to increase over time, approaching a maximum value when the jointly communicating system reaches thermodynamic equilibrium.

## Slide 13
 In a simple manner, the second law states "energy systems have a tendency to increase their entropy rather than decrease it." This can also be stated as "heat can spontaneously flow from a higher- temperature region to a lower-temperature region, but not the other way around." Heat can appear to flow from cold to hot, for example, when a warm object is cooled in a refrigerator, but the transfer of energy is still from hot to cold. The heat from the object warms the surrounding air, which in turn heats and expands the refrigerant. The refrigerant is then compressed, expending electrical energy. The entropy of an isolated macroscopic system never decreases. However, a microscopic system may exhibit fluctuations of entropy opposite to that stated by the Second Law

## Slide 15
As a system approaches absolute zero, all processes cease and the entropy of the system approaches a minimum value.
If the entropy of each element in some (perfect) crystalline state be taken as zero at the absolute zero of temperature, every substance has a finite positive entropy; but at the absolute zero of temperature the entropy may become zero, and does so become in the case of perfect crystalline substances.

## Slide 16
In simple terms, the Third Law states that the entropy of most pure substances approaches zero as the absolute temperature approaches zero. This law provides an absolute reference point for the determination of entropy. The entropy determined relative to this point is the absolute entropy.
Another application of the third law is with respect to the magnetic moments of a material. Paramagnetic materials (moments random) will order as T approaches 0 K. They may order in a ferromagnetic sense, with all moments parallel to each other, or they may order in an antiferromagnetic sense, with all neighboring pairs of moments antiparallel to each other. (A third possibility is spin glass, where there is residual entropy.)

## Slide 18
 Over the years, various thermodynamic researchers have come forward to ascribe to or to postulate potential fourth laws of thermodynamics (either suggesting that a widely-accepted principle should be called the fourth law, or proposing entirely new laws); in some cases, even fifth or sixth laws of thermodynamics are proposed. Most fourth law statements, however, are speculative and controversial.
 The most commonly proposed Fourth Law is the Onsager reciprocal relations, which give a quantitative relation between the parameters of a system in which heat and matter are simultaneously flowing.

## Slide 19
THANK YOU