## Slide 2: Why Non thermal?
The main problem with the thermal processing of food is loss of volatile compounds, nutrients, and flavour.
To overcome these problems non thermal methods came into food industries to increase the production rate and profit.
The non thermal processing is used for all foods for its better quality, acceptance, and for its shelf life.
The new processing techniques are mostly employed to the liquid packed foods when compared to solid foods.

## Slide 3
Since the non thermal methods are used for bulk quantities of foods, these methods of food preservation are mainly used in the large scale production.
The cost of equipments used in the non thermal processing is high when compared to equipments used in thermal processing.
After minimising the investment costs of non thermal processing methods, it can also be employed in small scale industries.

## Slide 4: NON-THERMAL PROCESS ARE:-











Ohmic Heating Microwave heating Radiofrequency heating Infrared heating
High Pressure Processing Pulsed Electric Field Ultrasonics
Pulsed Light Technology Pulsed X-rays Irradiation
Oscillating Magnetic Field

## Slide 5: Microwave Heating:
Refers to the use of electromagnetic waves of certain frequencies (2450MHz and 915MHz. )to generate heat in material.
Container with food is placed in a microwave oven
And then a oven is activated, the food at the edge of the container heats faster and a temperature gradient develops between the centre and the edges

## Slide 6: Mechanism
Dipolar interaction:
polar molecules such as water molecules(dipole) inside the food will rotate according to the alternating electromagnetic field.
The rotation of water molecules would generate heat for cooking
Ionic interaction :
Ionic compounds (i.e. dissolved salts) in food can also be accelerated by the electromagnetic field and collided with other molecules to produce heat

## Slide 8: PULSED ELECTRIC FIELD (PEF) TECHNOLOGY
PEF is a non-thermal food preservation technology that involves the discharge of high voltage electric pulses (up to 70 kV/cm) into the food product, which is placed between two electrodes for a few microsec

## Slide 9: HIGH PRESSURE PROCESSING: (HPP)
 High Pressure Processing is also known as “High Hydrostatic Pressure” or “Ultra High Pressure” processing. HPP uses up to 900MPa to kill many of the micro organisms found in foods, even at room temperature without degrading vitamins, flavor and colour molecules in the process .
Food packages are loaded onto the vessel and the top is closed.
The pressure medium usually water is pumped into the vessel from the bottom.

## Slide 10
 Once the desired pressure is reached, the pumping is stopped, valves are closed, pressure can be maintained without further need for energy input.
Principle:
A principle underlying HPP is that the high pressure is applied in an “isostatic” manner such that all regions of food experience a uniform pressure, unlike heat processing where temperature gradients are established.

## Slide 11: PULSED LIGHT (OR) HIGH INTENSITY LIGHT TECHNOLOGY :
High Intensity Light Technology can be used for the rapid inactivation of micro organisms on food surfaces, equipments and food packaging materials.
High intensity white light and UV light food preservation methods employ light wave lengths ranging from ultra violet to near infra-red in short intense pulse.
Pulses of light used for food processing applications typically emit one to twenty flashes per second of electromagnetic energy

## Slide 12
It is generally accepted that UV plays a critical role in microbial inactivation.
The treatment is most effective on smooth, nonreflecting surfaces or in liquids that are free of suspended particulates.
•
In surface treatments, rough surfaces hinder inactivation due to cell hiding.

## Slide 13: Ohmic heating

Ohmic heating is an advanced terminal processing method where in the food material which serves as an electrical resistor, is heated by passing electricity through Which result in rapid & uniform heating

Electrical resistance heating or joule heating or electro-heating
13

## Slide 14: Important benefits
Fast Processing
Homogeneous Treatment
More effective method
14

## Slide 15
15